DOCUMENTATION FOR PROGRAM SEARCH

 Program SEARCH is used to search the ICDD-JCPDS database to find 
 known phases matching a diffraction pattern from an unknown 
 materials, which may contain one or more phases. 

 When running program SEARCH, it is first necessary to set up the
 search by specifying the peak positions and the parameters which
 govern how the search will be performed. The READ command may
 be used to read in a peak/data file. As an alternative to supplying 
 peak positions from a file, peak positions may be input using the 
 EDIT command, which invokes the peak list editor. If SEARCH has 
 previously been run, the previous peaks and parameters may be 
 reloaded using command LOAD. 

 Search parameters may be modified using commands SET, STARTFILE, 
 and TITLE and displayed using command SHOW. 
 Peak positions and intensities may be modified using the EDIT command. 
 Units for peak positions may be d-spaces or two-theta angles, as 
 selected using the WAVELENGTH command. 
 The inclusion of deleted patterns may be set using command DELETED.

 After the search parameters have been set, the search is performed
 using command SEARCH, which is equivalent to entering commands
 REDUCE, MATCH and REPORT. ICDD-JCPDS entries which have been 
 selected as potential "hits" are written onto a file which may be 
 read by the LOGIC program. Command LOGIC starts this program and
 passes the file of "hits."
 A search consists of four steps:
   1  Setting the scope of the search -- restricting the 
	search to the entries in a ICDD-JCPDS subfile or by using 
	chemistry to constrain the search (command STARTFILE);
   2  Reducing the extent of the search by dropping entries that
	are unlikely to be "hits" (command REDUCE):
	-- by eliminating entries that do not have at least one strong 
	peak matching one of the observed strong peaks ["Required Lines"];
	-- by eliminating entries that have a strong peak in reqions 
	of the observed pattern where no significant intensity 
	is present ["Forbidden Lines"];
   3  Matching the remaining ICDD-JCPDS entries against the list of
	observed peaks -- ICDD-JCPDS entries with too many unmatched peaks
	or not matching a sufficient number of observed peaks are
	dropped; the remaining entries are written as a user subfile
	(command MATCH);
   4  Evaluating the the "goodness of fit" between each 
	remaining entries and the observed pattern -- optionally, 
	the remaining entries may be ranked and the entries with the 
	best fits may also be written as a user subfile (command REPORT).

  The SEARCH command performs steps 2, 3 and 4 and thus is equivalent 
  to using the REDUCE, MATCH and REPORT commands sucessively.
  These steps must be performed in order, but any step may be omitted.
===> COMMAND  DCL
 Spawns a subprocess to execute DCL commands, type LOGOUT to 
 return back to SEARCH loss of the current work. 
 This command is useful for quick DCL "errands" such as answering a 
 mail message without exiting the program.
===> COMMAND  DELETED
 Some of the entries in the database are marked as "deleted" by the
 editors of the database. If these entries are included in the database
 (using the ENCODE program, PDF1) it is possible to select that these
 entries will be included or excluded from the operations of this
 program. 

 This command causes logical name PS_DELETED to be set so that 
 subsequent operations with the program and with other programs in the
 Powder Suite package will use the same option. The default mode for
 the program is DELETED/EXCLUDE. However, if desired the PS_DELETED
 logical name may be predefined (see customization instructions) to change
 the default.
---  Qualifiers
/INCLUDE
 Specifies that deleted entries will be included in the logical operations.
/EXCLUDE
 Specifies that deleted entries will be not be included in the logical operations.
===> COMMAND  EDIT
Used to edit the list of peaks. Peaks may be added, deleted or changed.
This operation must be done interactively. Note that intensities may 
be input with an arbitrary scale, but will be normalized internally 
before use.
===> COMMAND  EXIT
 Type EXIT (which can be abbreviated to EX) to exit from the program.
 Alternately, pressing Control Z (^Z) will also cause the program 
 to exit. Either causes the current search information to be written 
 onto a load file (see commands SET/NAME and LOAD.)

 When the load file is written, logical device name SEARCH_FILE 
 is defined as the name of the load file. If program SEARCH is
 restarted in the same login session, the file defined by 
 SEARCH_FILE (if any) may be read. 
===> COMMAND  FILE
 Allows a series of commands to be input to the program from an external
 file. The file should be prepared before starting the program, or using
 the DCL command to invoke an editor. 
---  Parameter
file_name
 A single file may be specified on the command line containing the name
 of the file with commands. If the file is not specified, a prompt will be
 given to request a file name. 

 If no file extension is supplied, the default extension is .CMD
===> COMMAND  IGNORE
 This command is used to display and modify the range of angles/d-spaces 
 which are used when searching the ICDD-JCPDS database. The ranges that have 
 been set to be ignored are called "excluded regions." Peaks in a 
 ICDD-JCPDS entry which are located in an excluded region are ignored,
 e.g. their presence will not disqualify the entry in the REDUCE step,
 nor will they be counted as unmatched peaks. Similarly, observed peaks 
 which fall inside an excluded area are not used for searching and are
 not counted toward the percentage of matched peaks.

 Two common applications which require use of excluded regions are:
 (1) to insure that only peaks on ICDD-JCPDS entries within the observed
 two-theta region are used -- the regions below and above the measured
 diffraction pattern should be excluded. (2) to account for interference
 from known or identified phases. For example, if silicon is used as an
 internal standard, the silicon peaks could obscure a peak from an 
 unknown phase. Thus, the regions immediately surrounding the silicon 
 peaks should be treated as unknown and thus should be excluded from
 consideration.
 
 Qualifier /EXCLUDE is used to add or increase the size of an
 excluded region and /INCLUDE is used to reset a region
 so that it is no longer excluded. Qualifier /CARD is used to 
 exclude all peaks in a ICDD-JCPDS entries above a threshold intensity and
 Qualifier /DISPLAY is used to display the current list of excluded
 regions.

 When a raw datafile is read into this program, regions outside the range
 of the collected data are excluded. If a list of peaks is read from 
 a peak file without a datafile, the regions below the lowest angle 
 and above the highest angle are excluded. These excluded ranges may be 
 extended using /EXCLUDE and reduced using /INCLUDE. 
/DISPLAY
 Qualifier /DISPLAY produces a listing of the current "excluded regions". 
 If this qualifier is combined with other qualifiers, the excluded regions
 will be displayed after any changes.
/CARD=jcpds_card
/CARD
 Qualifier /CARD excludes regions surrounding a ICDD-JCPDS entry. If 
 supplied, jcpds_card is the 5 or 6 digit ICDD-JCPDS set and entry number 
 (e.g. /CARD=110011). The width of the region around each peak may be 
 specified using qualifier /WIDTH and the intensity threshold for 
 ignored peaks may be specified using /IMIN.
 Qualifier /CARD cannot be used with /INCLUDE or /EXCLUDE.
/IMIN=min_inten
 /IMIN specifies the minimum intensity for ICDD-JCPDS peaks which will be 
 "excluded". Peaks with relative intensity below min_inten (in units of
 % of the most intense peak) will not be used.
/INCLUDE=position_list
/INCLUDE
 Specifies a list of central points of regions which will be reset so 
 that these regions will no longer be "excluded" from the search. The 
 the length of each region will depend on the value of DEL_2THETA 
 (see /WIDTH.)

 More than one position may be specified by enclosing the list in
 parentheses and separating the points by commas, e.g.
      /INCLUDE=4.0 or
      /INCLUDE=(4.0,6.0)
 The units for position_list will be d-spaces in Angstrom, unless 
 a wavelength has be set, in which case the units will be degrees 
 two-theta at the current wavelength.

 Note that if /CARD has been used previously, all peaks that lie 
 in the region to be included will be no longer be excluded.
 Qualifier /INCLUDE cannot be used with /CARD or /EXCLUDE.
/EXCLUDE=position_list
/EXCLUDE
 Specifies the central point in the region to be "excluded" from the 
 search. The the length of each region will depend on the value of 
 DEL_2THETA (see /WIDTH.)

 More than one position may be specified by enclosing the list in
 parentheses and separating the points by commas, e.g.
      /EXCLUDE=4.0 or
      /EXCLUDE=(4.0,6.0)
 The units for position_list will be d-spaces in Angstrom, unless 
 a wavelength has be set, in which case the units will be degrees 
 two-theta at the current wavelength.
 Qualifier /EXCLUDE cannot be used with /INCLUDE or /CARD.
/WIDTH=D_2THETA
 D_2THETA defines the half width to be allowed around a position 
 specified using the /EXCLUDE or the /INCLUDE qualifiers or the
 ICDD-JCPDS peaks from a entry specified using the /CARD qualifier. The
 units for D_2THETA are degrees two-theta for Cu K alpha 1 
 radiation.  D_2THETA may be a floating point number.
===> COMMAND  LOAD
 This command is used to reload the output file ("load file") from 
 a previous run of SEARCH so that parameters may be easily 
 changed. Thus the search run may quickly repeated with a new set of 
 parameters, allowing the widening of a search that failed to find 
 any matching phases or narrowing of a search that yielded too many 
 unlikely matches.

 The "search name" (see command SET /NAME) is set as the name of 
 the LOAD file, after dropping the file extension, if one has been 
 supplied.
---  Parameter
file_name
 A single file may be specified on the command line containing the name
 of the file to be read. If the file is not specified, a prompt will be
 given requesting a file name to read. 

 The default file extension for the "load file" is .SEA_IN. 
===> COMMAND  LOGIC
 This command causes the SEARCH run to be terminated and program 
 LOGIC to be started. The results from the most recent search will 
 be passed to program LOGIC. The program will save the current SEARCH 
 parameters on a load file for future use before transferring control 
 to program LOGIC.
===> COMMAND  MATCH
 This command causes the program to invoke the MATCH step in the 
 search procedure. In this step peaks in the observed pattern are 
 compared line-by-line to the peaks in each possible hit remaining 
 after the REDUCE step (or in the starting subfile, if the REDUCE 
 step will be omitted). If the positions of two peaks (as two-theta 
 values for CuK alpha 1) agree within DEL_2THETA, the peaks are 
 considered to "match" (see SET/ERROR).

 For a JCPDS-ICDD entry to be retained by the MATCH step as a "hit" 
 all but DB_max_miss of ICDD-JCPDS peaks above DB_min_int percent
 relative intensity must be matched (see SET/DB_IMIN and SET/MAXDBMISS). 
 Also, at least OBS_min_lines percent of the lines above OBS_min_int
 percent relative intensity must be matched (see SET/MATCHOBS and
 SET/OBS_IMIN.
===> COMMAND  QUIT
 Type QUIT to exit from the program without writing a load file or 
 updating logical name SEARCH_FILE.
===> COMMAND  READ
 Reads a list of peak positions and optionally a raw data file. Peaks 
 in the peak list that are assigned to the K alpha 2 wavelength will be 
 ignored all others will be converted to d-spaces. 

 The "excluded regions", the ranges of d-spaces which are ignored 
 during searching, are reset by the READ command. (See command IGNORE  
 for more information about excluded regions). If peaks are input 
 without a data file, the regions of d-spaces outside the range of 
 peaks will be excluded. If a diffractogram is input as well, the regions 
 outside the range of collected data will be excluded rather than the 
 range of the data points (the collected data will usually cover a 
 signifcantly larger region than the range of peaks). If the 
 diffractogram will be used for FOM computations (see SET/FOM and
 REPORT), the background should be subtracted, prior to reading it in
 to SEARCH.

 The search name is defined from the peak file name (including 
 the device and directory if specified), but the file extension is 
 dropped. This file name is used to define the names of the "load 
 file," which is used for temporary storage of the current 
 SEARCH settings; the "search output file," which will contain
 a user subfile created with the matches from the search; a 
 "search report," if command REPORT is used to prioritize the 
 matches; and a "starting subfile," if the STARTFILE command is 
 used to spawn program LOGIC to create a subfile to narrow down the
 search using chemistry. See information on the SET /NAME 
 subcommand, for more information on file naming.
---  Parameter
file_name
 A single file may be specified on the command line containing the name
 of the file to be read. If the file is not specified, the program will 
 prompt for a file name to read.

 It is usually preferable to supply the file name without a file 
 extension, as the default extension will then depend on the file
 format. This improves the speed that the program has available 
 when searching for the file.
 The subroutines which read data and peak files, (subroutines 
 READDATA and READPEAK respectively), will attempt to determine 
 the format of the file from the file contents and the extension.
---  Qualifier
/FORMAT=fileform
 This optional qualifier may be used to specify the file format that will
 be used for reading the file.
 In most cases it is not necessary to specify the file format, as the 
 program will discern the file format from the file. However, in certain
 cases where problems are encountered, it may be necessary to use the 
 format option.
===> COMMAND  REDUCE
 This command causes the program to reduce the number of ICDD-JCPDS 
 entries that will be considered during the search by dropping entries 
 that are unlikely to be "hits" by performing two screening steps:
	entries are eliminated if they do not have at least one strong 
	peak matching one of the observed strong peaks ["Required Lines"];
	entries are eliminated if they have a strong peak in reqions 
	of the observed pattern where no significant intensity 
	is present [Forbidden Lines];
 The screening steps improve the speed of searching the database because they
 use the bitmap indices to eliminate rapidly from consideration entries that 
 cannot match the observed pattern. 
 
 The "Required Lines" screening step is governed by variables 
 Req_Index, R_Imin and DEL_2THETA, which are changed using command 
 SET (see qualifiers /R_INDEX, /Rmin and /Error). 
 This step looks up each peak in the observed pattern above 
 R_Imin% relative intensity in a peak index file selected by Req_Index.
 The peak positions in observed pattern and database must be within
 DEL_2THETA to match. Thus, patterns which do not have an observed peak 
 matching some peak in the JCPDS-ICDD database within DEL_2THETA will be 
 eliminated from further consideration as a potential match. 
 This screening step may be skipped, if desired, by setting Req_Index 
 to a value of 100 or greater.

 The "Forbidden Lines" screening step is governed by variables 
 Forbid_Index, F_Imin and DEL_2THETA, which are changed using command 
 SET (see qualifiers /F_INDEX, /Fmin and /Error). 
 This step elminates from further consideration entries in the JCPDS-ICDD 
 database that have strong peaks where no intensity has been observed. The
 peak index selected by Forbid_Index is searched for peaks in the regions
 of the observed pattern where there are no peaks above F_Imin/% relative 
 intensity within DEL_2THETA and that have not been "excluded". 
 Any JCPDS-ICDD entry with a peak in one of these regions will be 
 eliminated from further consideration as a potential match. 
 This screening step may be skipped, if desired, by setting Forbid_Index 
 to a value of 100 or greater.

 The REDUCE command need not be used, but if it will be used it must 
 be specified before MATCH (or REPORT, if MATCH will also be omitted.)
 Command SEARCH performs the REDUCE, MATCH and REPORT steps 
 sequentially.
===> COMMAND  REPORT
 Used to print a report on the matches from the previous search and/or
 creates a graph with the observed pattern and likely matching patterns.
 If the MATCH step was not performed first, the report may be run 
 using all entries in the current subfile (or those remaining after  
 removing entries in the REDUCE step). Note that the REPORT step 
 is usually rapid, but may take several minutes if more than a 
 thousand entries will be considered.

 For each entry, if two or more peaks match the observed pattern, 
 three or four figures of merit (FOM) are computed based on how 
 close the patterns match. The angle FOM reflects the descrepancies
 between matching observed and ICDD-JCPDS peak positions; the intensity
 FOM reflects the descrepancies between matching observed and ICDD-JCPDS 
 peak intensities; a full-pattern FOM is computed if a raw data file
 is input to this program; the overall FOM is computed from the 
 above FOM values.

 The formula used for the overall FOM depends on the setting for 
 Calc_type (see command SET/FOM).

  Following the computation of the FOM values and the optional sort
step, it is possible to display stick diagrams for the matching patterns
along with the observed peaks or the observed diffractogram for each pattern.
Patterns will be displayed by order of FOM, if sorted.

  The graphical display shows the observed peaks or diffractogram and 
an adjustable number of "hits." At the bottom of the page, the excluded
regions of the pattern and the "forbidden" regions of the pattern are
shown as two lines. If the graphics device supports display of more than 
one color on the screen. Different colors will be used to show excluded 
peaks. Otherwise, different line styles will be used.
---  Qualifiers
/PRINT
 Causes the report to be printed rather than displayed first on the
 terminal.
===> COMMAND  SEARCH
 This command causes the program to invoke the search procedure.
 The search may be performed interactively or in batch mode.
 If batch mode is selected, a load file will be written, 
 a batch job will be submitted and the program will then exit.
 The SEARCH command performs the equivalent of the following
 three commands: REDUCE, MATCH and REPORT 
---  Qualifiers
/BATCH
 This option causes the search to be performed in batch mode.
/INTERACTIVE
 This option causes the search to be performed interactively.
/PRINT
 Causes the report to be printed rather than displayed first on the
 terminal. Ignored if used with the /BATCH option.
===> COMMAND  SET
 This command is used to set parameters which govern the search.
 If SET is called with one or more qualifiers, the specified 
 parameters are updated and no prompts are generated. However, if
 SET is used with no qualifiers, prompts are generated which allow
 all parameters to be updated.

 When the search is performed (commands REDUCE, MATCH and REPORT), 
 peak positions from each appropriate entry in the ICDD-JCPDS database 
 are compared to positions from the list of peaks in the observed pattern. 
 Two peaks are considered to "match", if the two-theta values 
 agree within DEL_2THETA (see /ERROR). 

 In the MATCH step, observed and database entries are compared 
 peak-by-peak. If no observed peak matches for a ICDD-JCPDS peak and 
 the relative intensity of that peak is above DB_min_int percent, 
 (see /DB_IMIN), the peak is counted as a "miss." If more than 
 DB_max_miss ICDD-JCPDS peaks are not "missed"(see /MAXDBMISS), 
 the entry will be rejected. 
 Also in the MATCH step, the number of peaks in the observed pattern 
 which have been matched to ICDD-JCPDS are also counted. If fewer than 
 OBS_min_lines percent of the total observed peaks above OBS_min_int 
 percent relative intensity are matched, the entry is rejected. 
 Note that an observed peak may be matched by several ICDD-JCPDS lines, 
 and a ICDD-JCPDS line can be matched by several observed peaks.

 The speed of the search is improved through three optional steps.
 The first is by restricting the search to a ICDD-JCPDS or user subfile 
 created in program LOGIC (see command STARTFILE). The other two 
 methods utilize the strong peak indices to eliminate entries quickly 
 which have strong peaks where no intensity is observed (see /F_INDEX 
 and /Fmin, below) and/or to restrict the search to entries having at 
 least one strong line matching the an observed line in the pattern 
 (see /R_INDEX and /Rmin, below). The strong peak choices are utilized 
 in the REDUCE step, thus these parameters are ignored unless either 
 command REDUCE or SEARCH is used.
---  Qualifiers
/Error=DEL_2THETA
   DEL_2THETA defines the allowed discrepancy between peak positions 
   in the observed pattern and those in the database used in the 
   MATCH and REPORT steps.
   These steps match the peak positions using peak positions transformed 
   to angles for Cu K alpha 1 radiation. Thus, DEL_2THETA defines a
   discrepancy in units of degrees two-theta for Cu K alpha 1 radiation, 
   regardless of the wavelength mode (see command WAVELENGTH) used for 
   input of the peak positions.
 
   DEL_2THETA will typically be in the range 0.05 to 0.20 for most 
   searches. For materials where the lattice dimensions may vary (i.e. 
   solid solutions), or where either the observed peaks or the database 
   are presumed inaccurate, larger values may be needed.
/R_INDEX=Req_Index
/Rmin=R_Imin
 Req_Index and R_Imin determine how the "Required Lines" screening
 step in the REDUCE command is performed. In this step, entries from the 
 the starting subfile (see command STARTFILE) are dropped from 
 consideration unless one of the observed peaks matches a peak from 
 a peak index.
 This screening step may be skipped, if desired, by setting Req_Index 
 to a value of 100 or greater.

 Each non-excluded peak in the observed pattern with intensity above 
 R_Imin% of the strongest non-excluded observed peak will be checked 
 in this step to see if matches within DEL_2THETA of a peak in the 
 peak index selected by Req_Index. Thus, this step will reject from 
 further consideration as a potential match patterns that do not have at 
 least one observed peak matching some peak in the JCPDS-ICDD database.

 The allowed values for R_Imin are between 0 and 99. The allowed values 
 for Req_Index are between -1 and 100 and have the following meaning:
  	100 Skip the "Required Line" step.
  	-1  Use the "Three Strongest" Peak Index file.
  	n   Use the "n% and Above" Peak Index file (n = 0 to 99).
		   Note that if the requested index file is not available, 
		   the next smallest file (at 10% increments) will be used.

 R_Imin will typically be a fairly small number, 5-10%. For 
 patterns with many peaks, where the REDUCE step does not eliminate 
 many entries from consideration, it may be desirable to raise R_Imin
 up to the range of 25% or higher.

 Req_Index will typically be 70% or -1 ("Three Strongest") so that 
 only patterns with reasonably strong matching peaks will be located. 
 If there is fairly strong preferred orientation or other errors which 
 increase the likelyhood that strong peaks will not match between patterns,
 it may be necessary to use a lower value, 30% or 0%, for Req_Index.

 Likewise, when the range of excluded regions in the search becomes large,
 the probability that the excluded regions will contain all of the strong 
 peaks in the desired matching phase and thus the pattern will not be found.
 The likely situations where this may occur is when data were collected only
 over a small region of two-theta or when looking for a minor phase, where
 a large number of peaks in the pattern have already been identified.
 In these circumstances, if finding appropriate matches becomes difficult,
 lower Req_Index or even turn off this step (by setting Req_Index to 100).

/F_INDEX=Forbid_Index
/FWidth=FWHM
/Fmin=F_Imin
 Forbid_Index and F_Imin determine how the "Forbidden Lines" screening
 step in the REDUCE command is performed. In this step, entries from the 
 the starting subfile (see command STARTFILE) are dropped from 
 consideration if there is a peak in a peak index that falls in an area
 of the pattern where no peaks greater than F_Imin% are observed.

 In this step, the pattern is broken up into approximately 260 regions.
 Each region is checked to ensure that there are no peaks greater than 
 F_Imin% of the strongest non-excluded observed peak within FWHM
 degrees and that the region has not been marked as excluded. If there 
 are no peaks and no excluded regions, the peak index selected by 
 Forbid_Index is checked for peaks in this region. Any peak found 
 in the region will eliminate the entry from further consideration.

 The pattern is processed using using peak positions transformed 
 to angles for Cu K alpha 1 radiation. Thus, FWHM defines a width
 in units of degrees two-theta for Cu K alpha 1 radiation, 
 regardless of the wavelength mode (see command WAVELENGTH) used for 
 input of the peak positions.

 The allowed values for F_Imin are between 0 and 99. The allowed values 
 for Forbid_Index are between -1 and 100 and have the following meaning:
  	100 Skip the "Forbidden Line" step.
  	-1  Use the "Three Strongest" Peak Index file.
  	n   Use the "n% and Above" Peak Index file (n = 0 to 99).
		   Note that if the requested index file is not available, 
		   the next smallest file (at 10% increments) will be used.

 F_Imin will usually be a fairly small number, 1-4%, and
 Forbid_Index will typically be in the range of 30-50%. This implies that
 a JCPDS-ICDD peak in the range of 30-50% will be observed in the 
 experimental pattern at least at the 4% range. This may not be true
 if the specimen has extreme preferred orientation or is composed of several
 phases where no phase constitutes a majority of the sample or if the
 JCPDS-ICDD pattern has preferred orientation. In these cases, where the 
 REDUCE step leaves no reasonable materials as potential "hits", one 
 should lower F_Imin, perhaps as low as 0% and/or raise Forbid_Index 
 to 70-90% or -1. In extreme cases, for example, where one want to find
 matches to JCPDS-ICDD patterns where stong peaks may be completely missing 
 from the observed pattern, it may be necessary to skip this step (by setting
 Forbid_Index to 100.) For materials where the REDUCE step does not eliminate 
 enough entries from consideration, it may be desirable to raise F_Imin up 
 to the range of 10-15% and set Forbid_Index to 30%.
/MAXDBMISS=DB_max_miss
/DB_IMIN=DB_min_int
 In the MATCH step, the JCPDS-ICDD entries are compared one at at
 time to the observed peaks. The number of peaks in the JCPDS-ICDD
 pattern that must be matched for the entry to be given further 
 consideration is dictated by the values of DB_max_miss and
 DB_min_int. All JCPDS-ICDD entries that do not match this
 criteron are removed from the list of possible "hits."

 For a pattern to be considered a likely match for an entry one 
 expects most if not all of the strong peaks in the JCPDS-ICDD entry 
 to be observed. Weak peaks may not always be seen depending on the 
 relative amount of the phase and the quality of the sample and the 
 pattern. A pattern will be discarded if more than DB_max_miss peaks 
 above DB_min_int% relative intensity are not within DEL_2THETA 
 of an observed peak. Thus DB_min_int% determines the threshold 
 for what is considered to be an observable intensity level. If the 
 material is believed to be single phase, DB_min_int should be a 
 fairly larger number, 10-20%. But for identifying phases in a material
 with many phases, it may be necessary to raise DB_min_int as high as
 50%. Under circumstances, the observed peaks should match all of the
 JCPDS-ICDD peaks and DB_max_miss should be 0 or at most 1. However, 
 any of the following conditions can lead to strong JCPDS-ICDD peaks
 to be missing from an observed pattern: severe preferred orientation
 in the observed (or database!) pattern; an impurity in the database
 pattern (rare but sometimes occurs); peak shifts due to instrumental 
 errors. 

 In general it makes sense to start with small values for both
 DB_max_miss and DB_min_int. If no appropriate "hits"
 are found. It is advisible to raise first DB_min_int and then 
 DB_max_miss. Both values must be integers.
/MATCHOBS=OBS_min_lines
/OBS_IMIN=OBS_min_int
 In the MATCH step, the JCPDS-ICDD entries are compared one at at
 time to the observed peaks and patterns that do not match the observed
 pattern are removed from further consideration. Entries are removed
 unless at least OBS_min_lines percent of the lines above OBS_min_int
 percent relative intensity are matched.

 In general it makes sense to start with values in the range of 50% for 
 OBS_min_lines and 25% for OBS_min_int. Meaning that a database entry
 must match at least half of the observed lines above 25% relative 
 intensity. If the MATCH step fails to find any likely "hits," it is
 wise to lower OBS_min_lines and/or raise OBS_min_int so that fewer lines
 need to be matched for a hit to be obtained. Lower OBS_min_lines first, 
 if a multiphase mixture is suspected. 

 If too many "hits" are found to review conveniently, it is 
 wise to increase OBS_min_lines and/or lower OBS_min_int. If a 
 multiphase mixture is suspected, lower OBS_min_lines first.
/MAXCARDS=MAX_hits
 The MATCH step will be ended early if more than MAX_hits entries are 
 found in the search. This can be used to prevent "run-away" searches
 which turn up too many entries to comfortably review. When the search
 is performed interactively, the search can either be continued or
 abandoned if the MAX_hits threshold is reached.

 The default value for MAX_hits is 999. If this many entries are
 located, it is likely that the criteria for the REDUCE and MATCH
 are too broad and the run will need to be repeated. For very slow 
 computer systems or where CPU time is at a premium, it may be wise
 to lower this value. Under most conditions the value of MAX_hits
 is unimportant.
/SORT=Num_Sort
/SORT
/NOSORT
 This controls sorting of entries by figure of merit (FOM) in the 
 REPORT (or SEARCH) command. If Num_Sort is positive, the step 
 will list the Num_Sort ICDD-JCPDS entries with the best FOM and a subfile 
 with these entries will be written. If Num_Sort is zero or /SORT 
 is specified without a number for Num_Sort the sort will be performed 
 but all "hits" from the MATCH (or REDUCE step, if MATCH is 
 skipped) will be listed in the report. Using a negative value for 
 Num_Sort or specifying /NOSORT prevents sorting, speeding the REPORT
 step. 
/FOM=Calc_type
 Determines how the overall figure of merit (FOM) is computed in the
 Report command. 

 If Calc_type is 1, differences between matching observed and 
 ICDD-JCPDS peak positions do not affect the overall FOM. 

 If Calc_type is 2, differences between observed and ICDD-JCPDS 
 peak intensities do not affect the overall FOM. 

 If Calc_type is 3, the full-pattern FOM formula is used for the 
 overall FOM. This option is appropriate only if a raw data file has been 
 input to the program and also requires that the background be subtracted
 from the data before it is read into the program.
/NAME=search_name
 This qualifier is used to to define the names that will be used 
 for files that will be created during the run. While this name may
 be as long as 40 or more characters (VMS allows very long filenames),
 for convenience, the name will typically be 4 to 10 characters. The
 search name is subject to the normal VMS conventions governing 
 file names: all letters, numbers and some symbols (notably _ and -)
 are allowed, but spaces and most other symbols are not allowed. 
 
 If files are to be written in a directory or disk other than the
 current default, device specifications may be included in the 
 search_name. File extensions are allowed, but their use is 
 not recommended. If supplied, the file extension will be used for 
 naming the "load file" only.
 The following files are created by program SEARCH:
 
    The "load file" is used for temporary storage of the current 
	SEARCH settings. This file may be reread by a later run of
	SEARCH and will also be used if SEARCH is run as a batch job.
	The file name is taken from the search name. File extension
 	.SEA_IN is used, if none is specified in the search name.

    The "starting subfile" is created if the STARTFILE command 
	is used to narrow down the number of entries to be considered  
	during the search by creating a user supplied subfile. 
	The file is written by program LOGIC. The subfile to be written 
	will be named using the current search name, however, the 
	device/directory will be changed to the scratch directory, 
	PS_TMP, the string "_SEARCH" will be appended to the 
	search name, and the file extension will be set as .USRPDF.

    The "search output file"is a user subfile with the 
	matches (hits) from the search. This file may be read by 
	program LOGIC. The file will be named directly from the 
	search name; the file extension will be .USRPDF.
	
    The "top hits output file"is a user subfile with 
	the best ranked matches from the SEARCH or REPORT
	command if sorting has been requested. The file is the
	same as "search output file" except _TOPxx is appended
	to the search name (xx is the number of sorted entries).
===> COMMAND  SHOW
 This command is used to display the parameters which govern the 
 search, as established by command SET.
===> COMMAND  STARTFILE
 This command is used to select the entries in the ICDD-JCPDS database that
 will be considered when performing the search. The entire database
 may be searched or the search may be restricted to a smaller section 
 (subfile). A number of standard subfiles have been prepared by the
 ICDD-JCPDS; alternately program LOGIC may be used to prepare a 
 user-defined subfile. 

 Use of a subfile (any option other than /SUBPDF=FULL) reduces
 the number of entries that need be examined, which can greatly speed the 
 search. For example, if it can be assumed that no elements heavier 
 than iodine are present in the unknown, program LOGIC can be used to 
 eliminate approximately one-third of the entries in the database from 
 consideration. (This is performed using command
     	CULL/E_SP=(Xe,Lr)/OR
 within program LOGIC.)
 
 Program LOGIC is most commonly used to specify chemistry constraints.
 To call program LOGIC from within SEARCH, enter command STARTFILE/LOGIC.
 To read a subfile previously prepared by LOGIC and stored in a 
 user-defined file, use command STARTFILE/USERFILE=file_name to select 
 that file. The user-defined subfiles created at the end of SEARCH run 
 may also be used as a starting point.

 Only one of the following three options may be specified. 
---  Qualifiers
/LOGIC
Specify this qualifier to call program LOGIC to create a new 
user-supplied subfile to be used in the search. When the LOGIC 
program is exited, a subfile will automatically be written and 
program SEARCH will be resumed. 
The subfile to be written will be named using the current search 
name, however, the device/directory will be changed to the scratch 
directory, PS_TMP, the string "_SEARCH" will be appended to 
the search name, and the file extension will be set as .USRPDF. 
/USERPDF=file_name
Use a previously written user-supplied subfile with name file_name. 
The default file extension is .USRPDF.
/SUBPDF=sub_file
 Use this option to start from one of the standard subfiles, such as the
 the inorganic subfile.

 The available subfiles are: 
     FULL         all entries in the database
     NULL         null table (a table without any entries)
     INORGANICS   Inorganic materials
     ORGANICS     Materials with a C-H bond
     COMMON       commonly found materials or phases
     MINERALS     Minerals, natural and synthetic
     METALS       metals, alloys and related materials
     NIST         patterns recorded by NIST (NBS)
     FORENSIC     materials of forensic interest
     ZEOLITES     zeolites and molecular sieves
     DELETED      superceeded but not removed patterns (if any)
     LOCAL        locally defined patterns (if any)
     SUPERCON     superconductors and related materials
     EXPLOSIVES   explosives and related materials
     EDUCATION    educationally relevant materials
     CEMENT       materials related to cement production
     CORROSION    corrosion products and related materials
 Only one subfile may be specified. To search two subfiles, (for 
 example the MINERALS and METALS subfiles) use program LOGIC 
 (see /LOGIC) to OR (ADD) together these two subfiles.
  Note that the sub_file name may be abbreviated by only including
  the initial letters as long as the name is uniquely specified. Also
  note that "DELETED" patterns are not used unless the DELETED/INCLUDE
  command is used to force inclusion of these patterns.
===> COMMAND  TITLE
 Used to change the "search title." The only purpose of the search 
 title is to provide a mechanism for saving comments and other 
 information from a search in the "load file."

 The format of this command is:
      TITLE title
 The title can be specified on the command line or will be prompted.
 If the title is put on the command line, any lower case letters used 
 in the title will be converted to uppercase.
---  Examples
TITLE This is the new title for the search
			Note that the title will be converted to all 
			capital letters.
TITLE
			The user will be prompted to specify a title.
===> COMMAND  WAVELENGTH
 Peaks positions may be input or output as d-spacings (in Angstrom) or 
 as two-theta (Bragg) angles corresponding to a given x-ray or neutron 
 wavelength. This command is used to select between d-spacings 
 and angles and to select a wavelength for the latter option.

 The current mode of the program is displayed in the header line at the
 top of the computer screen. The default when the program is started 
 is determined by logical name PS_WAVELENGTH. If this logical name
 is not defined, the default is to operate in d-space mode. When
 the WAVELENGTH command is used logical name PS_WAVELENGTH
 is redefined and this becomes the new default mode.
---  Parameter
wave_length
  A single wavelength value may be specified directly, where wave_length 
  is the x-ray or neutron wavelength in Angstrom. (The target_type will be 
  assumed to be SY for synchrotron radiation).

  If 0.0 is used for the wave_length, the program will enter d-space 
  mode (equivalent to specifying (WAVELENGTH/NOTARGET).

  If wave_length is used, /TARGET and /WTYPE should not. 
---  Qualifiers
/TARGET=target_type
/TARGET
/NOTARGET
 Specifies an x-ray target for conventional x-ray sources. 
 The choices for targets are:
	 Cu, Mo, Ni, Co, Fe, Cr, Ag, NU, or SY. 
 Specifying /TARGET without a target_type is equivalent to 
 /TARGET=CU. (Capitalization of the target type is ignored.)
 If NU or SY (for neutron or synchrotron radiation) is used, 
 the program prompts for a wavelength. 

 For input/output using d-spacings specify /NOTARGET

 The /TARGET option cannot be specified with a wave_length value.
/WTYPE=wave_type
   wave_type may be either 1, 2 or 3 which determines 
   the exact value used for the wavelength specified with /TARGET.
   The choices are:
  	1 to use K alpha 1 radiation 
  	2 to use K alpha 2 radiation 
  	3 to use the intensity weighted average of K alpha 1 and K alpha 2 
	  radiation.
   Specifying /WTYPE without a value for wave_type is equivalent 
   to specifying /WTYPE=1.
   This qualifier is ignored if the radiation source has a single 
   wavelength, (e.g. /TARGET=NU or /TARGET=SY) or a 
   wave_length is specified.
---  Examples
WAVELENGTH/TARGET=CU/WTYPE=3
	The wavelength will be set to the average of Cu K alpha 1 and 
	K alpha 2.
WAVELENGTH/TARGET
	The wavelength will be set to Cu K alpha 1.
WAVE/NOTAR
	Peaks positions, etc. will be displayed as d-spaces.
WAVE 0.0
	Peaks positions, etc. will be displayed as d-spaces.
WAVE 2.5401
	The wavelength will be set to 2.5401Angstrom.
WAVE
	The user will be prompted to choose a wavelength or two use
	d-spacings. 
WAVELENGTH/TARGET=NU/WTYPE=3
	The user will be prompted to enter a wavelength; the /WTYPE=3
	qualifier will be ignored.